Magnepan MMG Ceiling Suspension Setup

The main idea behind this plan is to suspend the MMGs from the ceiling, at least two feet from the back wall for very good listening positioning. In doing so, the speakers are always at the same level from the floor as the listeners' ears, whether standing or sitting. Since Maggies are fussy about placement, I opted to use shelving tracks on the ceiling which would allow me to move the speakers to my heart's content. While it is ideal to have either nothing or something acoustically absorbent between the speakers, this was not practical in my situation.

Equipment used (all from Home Depot):

- Four wall-mountable metal shelving tracks

- Six toggle bolts

- Four four-inch springs, each capable of suspending 50 pounds

- Four four-foot lengths of chain, depending on ceiling height and desired speaker suspension height (I used white chain)

- Four connectors or fasteners which will attach to MMGs at existing screw holes

How to do it:

- Decide on placement for mounting shelving tracks to the ceiling. Mine allow for adjustments as close to one foot from the wall and as far as a few inches in front of the entertainment center.

- FIRMLY attach shelving tracks to the ceiling, either screwing directly into beams or using very large toggle bolts. (The MMGs weigh over 50 lbs. each.)

- Remove bottom screws from MMGs where the factory stands are meant to attach.

- Attach one fastener (see Figure 3) on each side of the speaker.

- Slide the spring into the desired hole in the shelving track.

- Attach one end of the chain to the other end of the spring, loop it through the fastener on the speaker, and attach the other end of the chain to the spring.

Figure 1: View from the floor to the ceiling:

Figure 2: View is from the main listening area toward the stereo setup:

Figure 3: View of fastener used to attach chain to MMG where factory stand is meant to attach

Figure 4: View is of one of the four tracks which are attached to the ceiling: